## Slide 1: CHIPP - CSCS F2F meeting
ETHZ, Zürich
September 1st , 2016

## Slide 2: Tier 2 status and plans CSCS
Statistics
  Availability/Reliability
  CPU usage
  Storage usage
Operations
  Updates
  Main Issues
Plans
  Phases of Phoenix
  Pledges
Open discussion:
  Memory Usage
  Support Changes

## Slide 3: Statistics

## Slide 4: Statistics
Two maintenances in one month (dCache issue)
Incident/Maintenance on IB network

## Slide 5: Statistics – CPU usage

## Slide 6: Statistics – Storage usage (2/2)
Allocated space
atlas 1377.6 TB
cms 1383.6 TB
lhcb 789.8 TB

## Slide 7: Operations

## Slide 8: Operations – Updates: Phoenix Services Overview

## Slide 9: Operations – Updates since march 2016:
  Cluster completely re-installed with Puppet
    still missing VO boxes
  All VMs services now running on CSCS VMware infrastructure
  New worked nodes installed and updated to v4
  New Slurm (v15.08) and ARC CE Setup. CREAM CE decommisioned
Partition | WNs | CPU | Cores
arc01 | wn[15-79] | Xeon(R) CPU E5-2670 0 @ 2.60GHz | 32
arc02 | wn[80-128] | Xeon(R) CPU E5-2680 v2 @ 2.80GHz | 40
arc03 | wn[129-167] | Xeon(R) CPU E5-2680 v4 @ 2.40GHz | 56
TOTAL | 149 |  | 6080
  All partition are shared between the VOs

## Slide 10: Operations – Updates since march 2016:
  BDII reinstalled in HA mode with Keepalived and floating Ips
    3 BDII with 3 floating ip and load distribution (Round Robin), in case of failure ip will be moved to the one alive
  perfsonar puppetized and reinstalled
  Using CSCS central log/dashboards/metrics facility
    Mirroring to log.lcg.cscs.ch, kibana.lcg.cscs.ch and graylog.lcg.cscs.ch
    Local elasticsearch instances/local kibana dashboards (Demo)
  Allocated 1PB to dCache
  Integrated the storage into the CSCS SAN
  New CHIPPonCRAY Scratch

## Slide 11: GPFS Reads last year

## Slide 12: GPFS Writes last year

## Slide 13: GPFS IOPS last year

## Slide 14: Scratch performance during high load

## Slide 15: Operations – Main issues
Inodes – April 2016
  Set quota limits user based on fileset
Net-IB – June
  Replaced few cables
  OFED upgraded and alined around the cluster
  Datagram mode enable everywhere
Lcg-util/Scratch – July
  Moved to gfal2-util (VO related config)
  GPFS tuning for the new load

## Slide 16: Plans

## Slide 17: Plans – Phases of Phoenix
2013
2014
2015
2016
Phase H
Phase J
Phase K
Phase L
2017
Phase M
NOW

## Slide 18: Plans – Pledges
Phase | Compute power pledged [HS06] | Storage pledged [TB]
Phase H – April 2014 | 26000 | 1800
Phase J – April 2015 | 35000 | 2300
Phase K – April 2016 | 49000 | 3070
Phase L – April 2017 | 62000 | 3500
Phase M – April 2018 | 72000 | 4000
Need to set pledges for Phase M
Plans for 2017
Storage:
Today 3.4 PB
Decommission ~0.8 PB
Buy ~1 PB
Total 3.6 PB
Pledge 3.5 PB
Cost ~250K CHF
Compute:
Today 69K HS06
Decommission 3% (~2K HS06)
Buy ~12K
Total 79K HS06
Pledge 62K HS06
Cost ~200K CHF
Scratch:
~ 6 new NSD servers for Scratch (Cost ~ 40K CHF)
GPFS License Cost ~ 60K CHF
Network:
Replacement of old IB switches (Cost ~30K CHF)
VMWARE (Cost ~20K CHF)
Notes: ----- Meeting Notes (08/03/16 12:04) -----
Change Phase J stoirage pledge to 2300 instead 2000

## Slide 19: Discussion

## Slide 20: Memory Usage
If a job ask for more than 2.0G in ARC01/ARC03 does make sense that SLURM allocates 2 CPUs?

## Slide 21: Support Changes
In order to improve the support CSCS is delivering we would like to propose:
Bi-weekly operations meetings (30’ phone call)
Common list of ALL open issues (tickets)
Discuss & re-prioritize (or even reject) requests based on priorities
Closer VO-Rep to CSCS relationship
Periodic 1-day visit on-site (Bern/PSI/anywhere) for CSCS to see the “world” through the VO-Rep’s eyes
Strengthen the understanding of each individual’s role. Develop ways to find problems sooner
Close the VO-Box discussion
Please send us your feedback!

## Slide 22: Thank you for your attention.